## Slide 1: 3D Printer Team 75
PowerPoint 1: Organize Team and Team Introduction

## Slide 2: Possible System Solutions
Use a single, high-resolution DLP projector
Use a laser with Cartesian motion
Use a pico projector with Cartesian motion

## Slide 3: Trade-Offs: Single Projector
Pros
Motion only in one axis
More precise
Flexibility in projector choice
Cons
High upfront cost with projector purchase
Finite printing area
Bulky

## Slide 4: Trade-Offs: Laser
Pros
Low cost
Flexible build area size
Cons
Motion in 3 axes
Less precise

## Slide 5: Trade Offs: Pico Projector
Pros
Low cost
Flexible build area size
Cons
Motion in 3 axes
Less precise

## Slide 6: Possible Subsystem Solutions: Resin Vat
Solution | Cost | Effectiveness | Advantage
Squeegee | Motor and Time | High | Level Layers
Sylgard 184 | $60 0.5 kg | High | Non Stick Surface
Teflon | $14 10 oz. | Med | Cheap and Easy to Use
Tilting | Motor and Time | Med | Peels
Gorilla Glass | $110 9"x9" | High | Peels w/o movement

## Slide 7: Possible Subsystem Solutions: Build Table
Solution | Cost | Effectiveness | Advantage
Aluminum No Coating | No Extra Cost | Low | No Cost
Increase Cure Time | Increase Build Time | Medium | Free
Coating of FEP | $10.00 per 6 in2 | High | Faster Build Times

## Slide 8: Possible Subsystem Solutions: Printer Control Software
 | B9 Creator | MiiCraft | Creation Workshop
Language | C++ | Python | C#
Cross-platform | ✓ | ✗ | ✓
Slicing Software | Custom | Skeinforge | Slic3r
G-Code Support | ✗ | ✓ | ✓
CAD File Input | STL | STL | STL, OBJ, 3DS
Able to Add Supports | ✓ | ✗ | ✓
Image Output | SLC | SVG | SVG

## Slide 9: Possible Subsystem Solutions: Computing Platform

## Slide 10: Governing Science
Photocurable resins are hardened by exposure to light in a systematic manner to produce a desired shape
The build is progressed in layers in the Z axis which is controlled by a linear motion system

## Slide 11: Standards
ISO 6983: G-Code
ATX 2.2 Motherboard Standard
Mini-ITX 2.0 Motherboard Standard
ATX Power Supply Standard

## Slide 12: Limitations
Build size and build resolution are directly proportional
    With a 1920 x 1080 pixel projector and 100μm build resolution the build area is 19.2mm x 10.8mm
Build area must be enclosed to prevent unwanted UV exposure

## Slide 13: Equations
volume of build
esolution of projector in x axis
esolution of projector in y axis
esolution of build
size of build area in x direction
size of build area in y direction
size of build area in z direction