## Slide 1: Project PAM Ref: SP14-75-3DPR
Daniel Olsen (CE), Nicholas Lowman (CE)
Casey Spencer (EE), Chance Baker (EE)
Jeffrey Burdick (ME)- PM

## Slide 2: Team 75 Organization
Figure 1. Project Organization

## Slide 3: Outline
Project Organization- JPB
Prerequisites and Definitions- NAL
Executive Summary- JPB
Market Gap, Criteria, and Specifications- CWB
Chassis Design and Standards- JPB
Functional Block Diagram- DMO, NAL
Printer Control Software- DMO
Timeline and Resources- CWS

## Slide 4: Executive Summary
Problem
  High resolution additive manufacturing is not accessible for hobbyists (under $1,000)
  Current hobbyist 3D printers are imprecise, fault-prone, and poorly documented
  Available PAM systems are inflexible, use proprietary hardware and software
Solution
  Libre
  Accessible to the hobbyist
  Precise and repeatable
  Flexible for the end user
  Off-the-shelf open-source hardware
  A thoroughly documented reference design

## Slide 5: Market Gap
Figure 2. Market Gap
Chart: System Cost with Respect to Area and Volume
| 10411.967999999997 | 9812.8835999999974 | 70553.949389535599 | 19354.799999999996 | 51103.123599999999 | 19516.089999999997 | 19516.089999999997 | 14251.5844 | 51612.799999999996 | 38588.632499999992 | 92903.039999999979 | 81522.417599999986 | 41290.239999999998 | 41290.239999999998 | 45774.101999999992 | 41290.239999999998 | 61249.877499999995 | 61161.167999999991 | 60967.619999999995 | 59516.009999999987
FDM | 2199 | 399 | 900 | 799 | 2565 | 1649 | 1299 | 899 | 1949 | 1549 | 2295 | 2195 | 1299 | 999 | 1688 | 799 | 2195 | 2399 | 2500 | 1399
PAM | 3375 | 3299 | 1999 | 499 | 399
Project PAM | 1000

## Slide 6: Top Down vs. Bottom Up

## Slide 7: System Block Diagram
Figure 6. Functional Block Diagram

## Slide 8: Chassis Design
Figure 4. Proposed chassis design
Figure 5. Isometric view
of proposed chassis

## Slide 9: Specifications
Table 1. Specifications
Geometry | Dimension/Tolerance
Build Volume Size | 192 mm x 216 mm x 216 mm
X and Y Axis Resolution | 0.100 mm
Minimum Layer Height | 0.015 ± 0.002 mm
Parallelism/Perpendicularity of a 20 mm cube | 0.050 mm
Dimensional Tolerance of a 20 mm cube | ± 0.050 mm

## Slide 10: Technical Drawings/Title Block
The Coupler was GD&T according to ISO standards.
A Title Block was created for the Open Source Hardware Community
Notes: GD&T (Geometric Dimensioning &Tolerance)
  Datum's are necessary when properly GD&Ting high quality parts
  The following are important details to
  Geometric Characteristic Symbols Tolerance, Characteristic, Symbol
  Material Conditions Terms & Symbols: MMC(M), LMC(L), RFS(none)
  Additional Symbols
We noticed that ISO s to use and acknowledge revisions made to a specific part. Community projects are so poorly documented that not even a basic title block exists within the Open Source Hardware Community.

## Slide 11: Vat Simulation
FEA Simulation (fixtures, bonds, forces) – experienced bonding issues
Notes: indicates the ribbed vat will not sway.
indicates the ribbed vat will sway.  (result of bonding issues)
(𝑑_(𝑖𝑠𝑝𝑙𝑎𝑐𝑒𝑚𝑒𝑛𝑡 𝑉𝑎𝑙𝑢𝑒𝑠)≤0𝑚𝑚) indicates the ribbed vat will not sway.
(𝑑_(𝑖𝑠𝑝𝑙𝑎𝑐𝑒𝑚𝑒𝑛𝑡 𝑉𝑎𝑙𝑢𝑒𝑠)≥0𝑚𝑚) indicates the ribbed vat will sway.  (result of bonding issues)

## Slide 12: Wire Diagram

## Slide 13: Hardware Software Interface

## Slide 14: Hardware Software Interface contd.

## Slide 15: Projector and Resin
Projector Qualities
  High Resolution DLP
  UV Filter Removal
  Throw Distance
Resin
  Test for Layer Thickness
  Test for Exposure Time

## Slide 16: Software Problems

## Slide 17: New Design

## Slide 18: Timeline

## Slide 19: Timeline & Budget
Phase | Start Date | End Date
Build | 2014-08-18 | 2014-09-26
Test | 2014-09-14 | 2014-11-07
Documentation and Presentation | 2014-11-14 | 2014-12-12
Table 3. Proposed timeline

## Slide 20: Summary
Problem Statement
  Current hobbyist 3D printers are imprecise and fault-prone
  High resolution additive manufacturing is currently not accessible for hobbyists (under $1,000)
  Available PAM systems use proprietary hardware and software
Our Solution
  A DLP PAM system can produce high quality and fast prints
  Use off-the-shelf open-source hardware
  Create a thoroughly documented reference design

## Slide 21: Acknowledgements
Dr. Spyros Tragoudas | Dr. Tod Policandriotes | Lakendria Kenner
Dr. Rasit Koc | Dr. Vidya Singh-Gupta | Scott J. Grunewald
Dr. Lizette Chevalier | Dr. Frances Harackiewicz | Eddie Krassenstein
Dr. James Mathias | Dr. Alan J. Weston | Austin Miller
Dr. James Mabry | Kay Purcell | Indiegogo Funders
Tim Attig | Joe Lennox | 

## Slide 22: References
Make: Ultimate Guide to 3D Printing
ISO 262:1998, ISO general purpose metric screw threads -- Selected sizes for screws, bolts and nuts.
DIN 103, ISO Metric Trapezoidal Screw Thread.
ANSI/NEMA MG 1-2011, Motors and Generators.
ISO 6983-1:2009, Automation systems and integration -- Numerical control of machines -- Program format and definitions of address words -- Part 1: Data format for positioning, line motion and contouring control systems.
ISO 10303-21:2002, Industrial automation systems and integration -- Product data representation and exchange -- Part 21: Implementation methods: Clear text encoding of the exchange structure.
ISO/ASTM 52915:2013, Standard specification for additive manufacturing file format (AMF) Version 1.1.
W3C, "XML 1.1 Extensible Markup Language (XML) 1.1 (Second Edition)," 16 August 2006. [Online]. Available: http://www.w3.org/TR/2006/REC-xml11-20060816/. [Accessed 16 April 2014].
W3C, "Scalable Vector Graphics (SVG) 1.1 (Second Edition)," 16 August 2011. [Online]. Available: http://www.w3.org/TR/SVG/. [Accessed 16 April 2014].
ISO/IEC 14882:2011, Information technology -- Programming languages -- C++.
E. Chu, "B9 Creator," Make: Ultimate Guide to 3D Printing, p. 93.
B9 Creations LLC, "B9 Creator GitHub," GitHub Inc., 2014. [Online]. Available: https://github.com/B9Creations/B9Creator. [Accessed 27 February 2014].
Rays Optics Inc., "MiiCraft User Guide," 2012. [Online]. Available: http://www.miicraft.com/web/assets/2012/11/MiiCraft-3D-printer-User-Guide.pdf. [Accessed 27 February 2014].
S. Hernandez, "Creation Workshop GitHub," GitHub Inc., 2014. [Online]. Available: https://github.com/Pacmanfan/UVDLPSlicerController. [Accessed 27 February 2014].
S. Hernandez, "Creation Workshop - SLA / FDM Slicer and Controller," Makerbot Industries LLC, 8 January 2013. [Online]. Available: https://www.thingiverse.com/thing:40778. [Accessed 27 February 2014].
Fabmetheus, "Skeinforge Vectorwrite," Demozendium, 17 July 2012. [Online]. Available: http://fabmetheus.crsndoo.com/wiki/index.php/Skeinforge_Vectorwrite. [Accessed 27 February 2014].